## Slide 1: CSC 3511 Security and Networking
Week 1, Lecture 1: Course Overview

## Slide 2: Course Personnel
Instructor: Dr. Zhonghao Liao
  Office: DH 436
  Email: liao@msoe.edu
  Office hours:
    Monday, Tuesday: 10:00 am – 11:00 am, 2:00 pm - 3:00 pm
    Thursday: 10:00 am - 11:00 am
    Wednesday, Friday: Knock on door or by appointment
  Please feel free to come over when I'm in the office
Watch the Canvas
    Assignments, reading materials, lecture notes

## Slide 3: Course Materials
Textbook:
  Computer Networking A Top-Down Approach, 9th edition (ISBN: 9780135429334)
  Internet Security: A Hands-on Approach 3rd Edition (ISBN: 978-17330039-6-4)
  Free: An Introduction to Computer Networks by Peter L. Dordal
    Link: https://intronetworks.cs.luc.edu/current2/html/index.html
  Free: Computer Networks: A Systems Approach by Larry Peterson and Bruce Davie
  Link: https://book.systemsapproach.org/index.html
Lecture slides, notes, quizzes, homework, labs, etc.: Canvas
Prerequisites: working knowledge of Python and Linux (Don’t worry if you don’t have a working knowledge)

## Slide 4: What’s the “Internet”?
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches:
forward packets (chunks of data) as “network core”
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps as “network edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 5: What can “Internet” do?
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
Provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 6: Postal System Analogy – Building Block 1: Something that moves data
Postal service needs a way to deliver letters: mailman, carrier pigeon, Pony Express, trucks, airplanes, etc.
Internet also needs a way to move bits: wires, fiber optics, radio waves, satellites, etc.
Risks in delivery: letters may get lost, opened by others, or delayed. Similarly, network packets can be lost, intercepted, or exposed.
Building block 1: wires
Notes: If you were to send a love letter by pigeon, what problems could happen? How is that similar to sending a packet on the Internet?

## Slide 7: Postal System Analogy – Building Block 2: Talking to the apartment complex (Local Communication)
Within one apartment complex, the mailman delivers letters room-to-room
This is like a Local Area Network (LAN), connecting devices inside the same building
People can talk to their neighbors without involving the post office.
Building block 1: wires
Building block 2: LAN
Notes: Compare with WiFi in a coffee shop or Ethernet in a dorm building. Everyone shares one “local complex.”

## Slide 8: Postal System Analogy – Building Block 3: Post offices connect complexes (Wide Communication)
A post office connects multiple apartment complexes
Letters can travel between complexes through the post office
This is like a Wide Area Network (WAN), connecting LANs together.
Building block 1: wires
Building block 2: LAN
Building block 3: wide area network
Notes: My apartment → local mail delivery → post office → other apartments.

## Slide 9: Postal System Analogy – Internet Scale: Connecting the whole world
Multiple post offices around the world connect into a giant global system
A letter may pass through several post offices before reaching its destination
The Internet is the same: messages (packets) hop across multiple routers/ISPs before arriving.
Building block 1: wires
Building block 2: local network
Building block 3: the Internet

## Slide 10: Internet: Layers of abstraction
Layer 3: Connect many local networks to form a global network
Layer 2: Create links in a local area
Layer 1: Move bits across space => within single computer, or between computers
A change in one layer (e.g., switch pigeons to trucks) doesn’t break the others.
Internet layers:
  Application (email, web page)
  Transport (TCP, UDP)
  Network (IP)
  Link (WiFi, Ethernet)
  Physical (cables, wireless signals)
Postal system layers:
  Letter (content you wrote)
  Envelope (addressing)
  Mail carrier (physical delivery)
  Post office routing (deciding the next hop)

## Slide 11: Internet layering
Internet design is partitioned into various layers. Each layer…
  Has protocols
  Relies on services provided by the layer below it
  Provides services to the layer above it
Analogous to the structure of an application and the “services” that each layer relies on and provides
System Calls
Run-Time Library
Code You Write
Device Drivers
Hardware
Fully isolated from user programs

## Slide 12: Internet layering: OSI vs. TCP/IP model
Open Systems Interconnection (OSI) model:
  A theoretical, academic model of Internet communication
  Originally divided into 7 layers - But layers 5 and 6 aren’t used in the real world, so we ignore them
Same reliance upon abstraction
  A layer can be implemented in different ways without affecting other layers
  A layer’s protocol can be substituted with another protocol without affecting other layers
3. Network Layer
4. Transport Layer
7. Application Layer
2. Data Link Layer
1. Physical Layer
6. Presentation Layer
5. Session Layer
Layer 1 & 2 are closer to hardware (hardware + firmware):
signals, frames, MAC addresses
Layer 3 – 7 are closer to software:
logical addressing, connections, applications
Notes: Application Layer: Provides network services directly to user applications (e.g., HTTP, FTP, SMTP).
Presentation Layer: Translates data formats, handles encryption, compression (e.g., SSL/TLS, JPEG, MPEG).
Session Layer: Manages sessions between applications (start, maintain, terminate connections).
Transport Layer: Provides reliable or unreliable end-to-end delivery (e.g., TCP, UDP).
Network Layer: Handles logical addressing and routing (e.g., IP, ICMP).
Data Link Layer: Responsible for node-to-node delivery, framing, error detection (e.g., Ethernet, Wi-Fi).
Physical Layer: Transmits raw bits over physical medium (cables, radio, fiber optics).
OSI Layers Explained
Physical Layer (Layer 1)
Purely hardware: cables, fiber optics, radio waves, network cards (NIC transceivers).
Concerned with voltages, light pulses, frequencies, connectors.
Data Link Layer (Layer 2)
Very close to hardware, often implemented in NIC firmware and device drivers.
Handles framing, MAC addressing, and error detection (Ethernet, Wi-Fi).
A mix: partly hardware (chipsets, switches) and partly software (drivers, low-level protocols).
Network Layer (Layer 3) and above
Primarily software (routing algorithms, IP addressing, TCP logic, HTTP server software).
Implemented in the operating system’s networking stack or in application code.
Can be accelerated with hardware (e.g., routers have ASICs for IP forwarding, TLS offload cards for encryption).

## Slide 13: Internet layering: OSI vs. TCP/IP model
Transmission Control Protocol/Internet Protocol (TCP/IP) model:
  Practical model used on today’s Internet  Layers 5 (Session) + 6 (Presentation) are usually bundled into Application in TCP/IP
Different models, same idea  networking is layered abstraction, where each layer provides services to the one above
We follow the TCP/IP model (aka the Internet protocol suite model)to organize course content
3. Network
4. Transport
7. Application
2. Data Link
1. Physical
6. Presentation
5. Session
OSI
3. Internet (Network)
4. Transport
5. Application
2. Link
1. Physical
TCP/IP
IP, ICMP
TCP, UDP
HTTP, FTP, SMTP, DNS
SSL/TLS, JPEG, MPEG
RPC, NetBIOS
Ethernet, Wi-Fi
Typical Protocols & Technologies
Copper, Fiber, Radio
Notes: TCP/IP Layers Explain:
Physical Layer (Layer 1)
Pure hardware components: cables, fiber optics, wireless signals, connectors.
Transmits raw bits as voltages, light pulses, or radio waves.
Network Interface Cards (NICs) contain transceivers that handle this layer.
Data Link Layer (Layer 2)
Still close to hardware; often handled by NIC firmware and drivers.
Provides framing, MAC addressing, and error detection (e.g., Ethernet, Wi-Fi).
Mix of hardware and software: switches and NIC chipsets (hardware), drivers/protocol logic (software).
Network Layer (Layer 3)
Mostly software logic in the operating system.
Handles logical addressing (IP), routing, and forwarding.
Routers accelerate this with specialized hardware (ASICs).
Transport Layer (Layer 4)
Software-managed connections between applications.
Ensures reliable or best-effort delivery (TCP, UDP).
Runs inside the OS networking stack; some features can be offloaded to hardware (e.g., checksum).
Application Layer (Layer 5 in TCP/IP)
Directly visible to users and applications (HTTP, DNS, FTP, SMTP).
Includes higher-level logic like web browsers, servers, chat apps.
Can include encryption/compression (TLS, application data formats).

## Slide 14: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Protocols are everywhere
  Control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4/5G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force

## Slide 15: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 16: What’s a protocol – A Human Analogy
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Important points:
Distributed entities, exchanging messages (governed by protocols)
Time going down
How to define a protocol? (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 17: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 18: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software is a (free) packet-sniffer

## Slide 19: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 20: Network Threats & Attacks
people
application
session
transport
network
data link
physical
IP
TCP
email, Web, NFS
RPC
802.11
Sendmail, FTP, NFS bugs, chosen-protocol and version-rollback attacks
SYN flooding, RIP attacks,
sequence number prediction
IP smurfing and other
address spoofing attacks
RPC worms, portmapper exploits
WEP attacks
Only as secure as the single weakest layer…
… or interconnection between the layers
RF
RF fingerprinting, DoS
Phishing attacks, usability

## Slide 21: Network Defenses
Cryptographic primitives
Protocols and policies
Implementations
Building blocks
Blueprints
Systems
RSA, DSS, SHA-1…
TLS, IPsec, access control…
Firewalls, intrusion
detection…
All defense mechanisms must work correctly and securely
End uses
People
Password managers,
company policies…

## Slide 22: Why do we need security and HOW TO?
Scenarios: Trade secrets, medical records
  Requirements: Protect vital information secret while still allowing access to those who need it (Confidentiality)
  How to: Encrypted communications, secure transactions
Scenarios: Ensure data integrity and prevent unauthorized modification
  Scenarios: Financial transactions, software updates, legal documents
  Requirements: Ensure data integrity and prevent unauthorized modification
  How to: Digital signatures, Message authentication codes (MAC)

## Slide 23: Why do we need security and HOW TO?
Scenarios: Online banking, confidential email access, restricted databases
  Requirements: Provide authentication and access control for resources
  How to: Multi-factor authentication (MFA), public key infrastructure (PKI), biometric verification
Scenarios: Cloud services, e-commerce platforms, critical infrastructure systems
  Requirements: Guarantee availability of resources
  How to: Redundant systems, load balancing