## Slide 1: CSC 3511 Security and Networking
Week 4, Lecture 1: Transport Layer and TCP

## Slide 2
Roadmap
Reliable data transmission
TCP implementation: TCP connection setup
TCP implementation: RTT estimation
TCP implementation: Byte notation, segments, sequence numbers & ACK number

## Slide 3
Layer 3 (Network/IP) gave us the ability to send packets anywhere on the Internet
Abstraction level: Packets individually sent through the network
Problem: IP offers best-effort delivery
  Packets can be lost, corrupted, reordered, delayed, or duplicated
Problem: Applications don't want to think about packets and best-effort
  Programmers want to think in terms of a more convenient abstraction
Layer 4 (Transport) builds extra features on top of Layer 3
UDP (User Datagram Protocol): Adds de-multiplexing only
TCP (Transmission Control Protocol): Adds de-multiplexing and reliability
Both protocols provide a more useful abstraction to programmers
Let's check out each of these features
Transport Layer Protocols

## Slide 4
3 different levels of reliability:
Best-effort delivery
At-least-once delivery: Every packet arrives, but some might arrive more than once (duplicates)
Exactly-once delivery: Every packet arrives exactly once
Our plan for bridging the abstraction gap:
At transport layer: Use IP (best-effort delivery) to build at-least-once delivery
Then, get rid of duplicates and pass the result to the application This gives the application exactly-once delivery
Defining Reliability
We have to deal with 5 problems from the best-effort service model:
Packets can be dropped
Packets can be corrupted
Packets can be delayed
Packets can be duplicated
Packets can be reordered

## Slide 5
Designing Reliability for a Single Packet
Problem 1 - Packets can be dropped:
  The packet is sent. How does the sender know if it was received successfully?
Solution: The recipient replies with an acknowledgment (ack)
  Set a timer when we send the packet
  If the timer expires and we don’t get the ack, resend the packet
  When we get the ack, cancel the timer
ack
Sender
Recipient
Start timer
Timeout!
Restart timer
✗
Cancel timer

## Slide 6
Designing Reliability for a Single Packet
Problem 1 - Packets can be dropped:
  What if the ack gets dropped
The timer expires, and the packet gets resent. Repeat until the ack arrives.
The destination received the packet twice, but that's okay (at-least-once delivery).
ack
Sender
Recipient
Start timer
Timeout!
✗
Cancel timer
ack
Restart timer
Notes: How do we set the timer length?
Too long: Delays delivery.
Too short: Causes unnecessary retransmission.
Ideally: Timer is proportional to RTT (round-trip time).
Intuition: RTT is when you expected to see the ack.
In practice: Measuring the RTT is non-trivial.
RTT varies depending on what path the packet takes.
RTT varies along a fixed path: packet could get stuck in queues at links.

## Slide 7
Designing Reliability for a Single Packet
Problem 2 - Packets can be corrupted:
  The packet is sent. How does the sender know if it was received successfully?
Solution: The recipient calculates the checksum
  When you get a corrupt packet, ignore it (don't send the ack)
  Sender times out and resends
  Alternative solution: When you get a corrupt packet, send a negative acknowledgement (nack)
ack
Sender
Recipient
✗ Bad checksum
Timeout!

## Slide 8
Designing Reliability for a Single Packet
Problem 3 - Packets can be delayed:
  Minor delay: No problem. The ack still arrives before the timeout.
ack
Sender
Recipient

## Slide 9
Designing Reliability for a Single Packet
Problem 3 - Packets can be delayed:
  Longer delay: Sender times out and resends
  Aka, premature timeout
  The sender receives two acks. That's fine  The recipient will handle duplicate packets
ack
Sender
Recipient
Timeout!
ack

## Slide 10
Designing Reliability for a Single Packet
Problem 4 - Packets can be duplicated:
  The recipient gets the packet twice, and the sender receives two acks
  Why would the network even duplicate a packet? Usually, because of link-level reliability gone wrong (very rare)
  The recipient will handle duplicate packets
ack
Sender
Recipient
ack

## Slide 11
Designing Reliability for Multiple Packets
Problem 5 - Packets can be reordered (not relevant in single-packet case):
  For problem 1 to 4: We can use the single-packet solution repeatedly to support sending multiple packets
  One extra design component: sequence numbers
    Label each packet with a unique, increasing number
    Label each ack with which numbered packet is being acked
    Solve reordering – use numbers to reorder packets
    Solve duplication – use numbers to identify duplicate packets
Sender
Application
Recipient
Application
4. was the style
5. at the time
2. onion to my
3. belt, which
Out of order. Use numbers to rearrange.
1. So I tied an
1. So I tied an
Duplicates Same number

## Slide 12
Roadmap
Reliable data transmission
TCP implementation: TCP connection setup
TCP implementation: RTT estimation
TCP implementation: Byte notation, segments, sequence numbers & ACK number

## Slide 13
TCP State
Reliability requires maintaining state at the end hosts
Sender has to remember:
  Which packets have been sent and not acked?
  How much longer on the timer before I resend a packet?
Receiver has to buffer the out-of-order packets
State is maintained at the end hosts (sender and receiver), not in the network
In each separate connection, both end hosts need to maintain state
How to build a connection?
  TCP 3-way handshake

## Slide 14: TCP Connection Setup: Three-Way Handshake
Before exchanging data, sender/receiver “handshake”:
Agree to establish connection (each knowing the other willing to establish connection)
Agree on connection parameters (e.g., initial sequence number (ISN))
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: The TCP sender and receiver have a number of pieces of shared state that they must establish before actually communicating
FIRST they must both agree that they WANT to communicate with each other
Secondly there are connection parameters – the initial sequence number and the initial receiver-advertised bufferspace that they’ll want to agree on
This is done via a so-called handshake protocol – the client reaching our to the server, and the server answering back.
And before diving into the TCP handshake protocol, let’s first consider the problem of handshaking, of establishing shared state.

## Slide 15
TCP Connection Setup: Three-Way Handshake
Goal: Each host tells its ISN to the other host
SYN. Client says: "My ISN is x."
SYN-ACK. Server says: “I received x (expecting x+1 next). Also, my ISN is y.”
Connections in TCP are full-duplex:
  Both hosts can send data, and both hosts can receive data
  A can send to B, and B can send to A, simultaneously, in the same connection
ACK. Client says: "I received y (expecting y+1 next)."
After the three-way handshake, both sides can start sending data
SYN-ACK. seq=y, ack=x+1
Client
Server
SYN. seq=x
ACK. ack=y+1

## Slide 16
SYNbit=1, Seq=x
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
ACKbit=1, ACKnum=y+1
The final ACK (3rd) acts as a confirmation mechanism to ensure that:
  Both client and server are synchronized and aware of the connection state
  No data is transmitted before the connection is fully established, avoiding the acceptance of duplicate data
  The server only considers the connection fully established once the client sends the final ACK
  Out-of-sync states are avoided because both sides explicitly confirm that the connection setup is complete
TCP Connection Setup: Three-Way Handshake
Notes: How the 3-way handshake solves the above problems:
1. Half-Open Connection Problem:
In a 2-way handshake (without the final ACK), if the client terminates the connection or loses communication while the server still thinks the connection is active, this can result in a half-open connection. This leaves the server wasting resources maintaining a connection that no longer exists.
In the 3-way handshake, the final ACK step serves as a confirmation that the client is ready to proceed:
  If the client never sends this final ACK (due to termination or network failure), the server will not consider the connection established and will not continue waiting for data from the client.
  This prevents the server from being left with a half-open connection.
2. Duplicate Data Acceptance Issue:
In a 2-way handshake, the client might send data after receiving the first acknowledgment from the server, but due to retransmission of the connection request, the server might forget the initial connection and reprocess the data, resulting in duplicate data being accepted.
In the 3-way handshake, the final ACK step (client acknowledging the server) ensures that both the client and server are fully synchronized:
  The server only starts accepting data once it receives the client’s final ACK (step 3), confirming that the connection is fully established on both sides.
  This ensures that any retransmitted connection requests are handled before data transmission starts, preventing the server from accepting duplicate data.
3. Out-of-Sync Connection States:
In the 2-way handshake, there is no final confirmation that both sides have successfully synchronized their connection states. This can lead to situations where the client believes the connection is established, but the server either hasn't received the initial request or has forgotten it due to retransmissions.
In the 3-way handshake, the final ACK from the client ensures that the server knows the connection has been acknowledged by the client:
  Once the server receives this final ACK, both sides have confirmed that they are ready to communicate.
  Any subsequent data transmissions occur after both sides have agreed on the connection state, reducing the chance of out-of-sync states.

## Slide 17
TCP Connection Teardown
Normal termination:
Each side sends a FIN packet to say: "I'm done sending, but will keep receiving."
FIN packets must be acked, just like any other data.
When only one side has sent FIN, the connection is half-closed.
When both sides have sent FIN (both done sending), the connection is closed.
ACK
Client
Server
FIN
ACK
FIN
Just for fun: Abrupt termination can be used instead (e.g. in case of error):
Send a RST (reset) to say: “I will no longer send or receive data.”
RST packets do not need to be acked
Any data in flight is lost
If the RST sender receives more data later, send another RST
Client
Server
RST
data
RST
Notes: Abrupt termination is not something you need to know. Just for fun

## Slide 18
Roadmap
Reliable data transmission
TCP implementation: TCP connection setup
TCP implementation: RTT estimation
TCP implementation: Byte notation, segments, sequence numbers & ACK number

## Slide 19
TCP timeout and round trip time (RTT)
Problem 1 - Packets can be dropped:
Solution: Sender sets a timer; The recipient replies with an ack
How to set TCP timeout value?
Solution: Use RTT (round trip time) to estimate
ack
Sender
Recipient
Start timer
Timeout!
✗
Cancel timer
ack
Restart timer
Timeout:
Waiting time for an ACK
Detect lost segments: the sender relies on the timeout to notice the absence of an ACK
Ensure timely retransmission
Q: how to estimate RTT?
Too short: premature timeout, unnecessary retransmissions
Too long: slow reaction to segment loss
Notes: How do we set the timer length?
Too long: Delays delivery.
Too short: Causes unnecessary retransmission.
Ideally: Timer is proportional to RTT (round-trip time).
Intuition: RTT is when you expected to see the ack.
In practice: Measuring the RTT is non-trivial.
RTT varies depending on what path the packet takes.
RTT varies along a fixed path: packet could get stuck in queues at links.

## Slide 20
TCP timeout and round trip time (RTT)
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  Ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  Average several recent measurements, not just current SampleRTT
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average (EWMA)
Influence of past sample decreases exponentially fast
Typical value:  = 0.125
Notes: This is how TCP re-computes the estimated RTT each time a new SampleRTT is taken.
The process is knows as an exponentially weighted moving average, shown by the equation here.
Where alpha reflects the influence of the most recent measurements on the estimated RTT; a typical value of alpha used in implementations is .125
The graph at the bottom show measured RTTs between a host in the Massachusetts and a host in France, as well as the estimated, “smoothed” RTT

## Slide 21: TCP timeout and round trip time (RTT)
Timeout interval: EstimatedRTT plus “safety margin”
  Large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/TCP_RTT.php
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
(RTT deviation)
Notes: Given this value of the estimated RTT, TCP computes the timeout interval to be the estimated RTT plus a “safety margin”
And the intuition is that if we are seeing a large variation in SAMPLERTT – the RTT estimates are fluctuating a lot - then we’ll want a larger safety margin
So TCP computes the Timeout interval to be the Estimated RTT plus 4 times a measure of deviation in the RTT.
The deviation in the RTT is computed as the eWMA of the difference between the most recently measured SampleRTT from the Estimated RTT

## Slide 22
Roadmap
Reliable data transmission
TCP implementation: TCP connection setup
TCP implementation: RTT estimation
TCP implementation: Byte notation, segments, sequence numbers & ACK number

## Slide 23
Notation Change: Bytes vs. Packets
So far, we've used packets as the primary unit of data:
Each packet has a number
Acks reference packet numbers
TCP is implemented with bytes as the primary unit of data
Each byte has a number  Packets (number) are defined by the number of the first byte inside
ACKs reference byte numbers
You should be prepared to reason in terms of either.

## Slide 24
TCP Segments
TCP provides a reliable, in-order bytestream
We have to split this bytestream into packets
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Sender Application
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application

## Slide 25
TCP Segments
A segment is sent when the segment is full (max segment size),
or when the segment is not full, but times out waiting for more data
TCP Segment
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Sender Application
TCP Segment
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
TCP header carries a sequence number indicating where in the bytestream this segment fits.

## Slide 26
TCP Segments
TCP/IP packet: IP packet with TCP header and TCP data inside
Size limits (RFC 879 standard):
IP packet: Maximum transmission unit (MTU, e.g., 1500 bytes)
TCP segment: Maximum segment size (MSS)
MSS = MTU – (IP header) – (TCP header)
TCP Header
TCP Payload (Segment)
IP Header
IP Payload
Limit MTU bytes
Limit MSS bytes

## Slide 27
TCP Sequence Numbers
Numbering starts at a randomly-generated Initial Sequence Number (ISN)
First byte is ISN+1, then ISN+2, etc.
Starting at a randomly-chosen ISN is very important for security!
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
Sender Application

## Slide 28
TCP Sequence Numbers
The sequence number of a segment is the number of the first byte in the segment
Example: In the segment below, the sequence number is ISN + 140
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
Sender Application

## Slide 29
TCP ACK Numbers
The ack number indicates the next expected byte (i.e. the first unreceived byte)
Example: All bytes up to (and including) ISN + 219 have been received, so the next unreceived byte is ISN + 220
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Sender Application
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
Ack: ISN + 220

## Slide 30
TCP Sequence and ACK Numbers
The sequence number of a segment is the number of the first byte in the segment
Sender sends a packet with sequence number j
The packet contains B bytes
Bytes in the packet are numbered: j, j+1, j+2, j+3, ..., , j+B–1
Recipient sends a cumulative ack (number of highest byte received, plus one)
If all prior data is received, ack number is j+B.
Think of this as the next expected byte, or the first unreceived byte.
If earlier data before this packet is missing, the ack number will be lower (Retransmit)

## Slide 31
TCP Sequence and ACK Numbers
Assuming only one packet in flight, all packets length B, and no loss:
The last ack number is equal to the next sequence number.
"I expect j + B next." → "I'm sending j + B."
Sender
Recipient
ack = j + B
seq = j
seq = j + B
ack = j + 2B
seq = j + 2B
Q: What if the packet loss happens?
Sender’s packet is lost
ACK is lost

## Slide 32: TCP: Retransmission Scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: To cement our understanding of TCP reliability, let’s look a a few retransmission scenarios
In the first case a TCP segments is transmitted and the ACK is lost, and the TCP timeout mechanism results in another copy of being transmitted and then re-ACKed a the sender
In the second example two segments are sent and acknowledged, but there is a premature timeout e for the first segment, which is retransmitted. Note that when this retransmitted segment is received, the receiver has already received the first two segments, and so resends a cumulative ACK for both segments received so far, rather than an ACK for just this fist segment.

## Slide 33: TCP: Retransmission Scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: And in this last example, two segments are again transmitted, the first ACK is lost but the second ACK, a cumulative ACK arrives at the sender, which then can transmit a third segment, knowing that the first two have arrived, even though the ACK for the first segment was lost

## Slide 34: TCP Fast Retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: Let’s wrap up our study of TCP reliability by discussing an optimization to the original TCP known as TCP fast retransmit,
Take a look at this example on the right where 5 segments are transmitted and the second segment is lost. In this case the TCP receiver sends an ACK 100 acknowledging the first received segment.
When the third segment arrives at the receiver, the TCP receiver sends another ACK 100 since the second segment has not arrived. And similarly for the 4th and 5th segments to arrive.
Now what does the sender see? The sender receives the first ACK 100 it has been hoping for, but then three additional duplicate ACK100s arrive. The sender knows that somethings’ wrong – it knows the first segment arrived at the receiver but three later arriving segments at the receiver – the ones that generated the three duplicate ACKs – we received correctly but were not in order. That is, that there was a missing segment at the receiver when each of the three duplicate ACK were generated.
With fast retransmit, the arrival of three duplicate ACK causes the sender to retransmit its oldest unACKed segment, without waiting for a timeout event. This allows TCP to recover more quickly from what is very likely a loss event
specifically that the second segment has been lost, since three higher -numbered segments were received