## Slide 1: CSC 3511 Security and Networking
Week 5, Lecture 2: Forwarding and Routing

## Slide 2
Roadmap
Packet Forwarding
Define the Routing Problem
Routing Protocol: Link State

## Slide 3
Review: Router Architecture
Generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
Forwarding, data plane (hardware): operates in nanosecond
Routing, control plane (software): operates in millisecond time frame
Input port
(e.g.,
Ethernet)
Output port
(e.g.,
Ethernet)
Input ports and output ports are connected via switching fabrics

## Slide 4: Switching fabrics
Bus: Datagram forwarded via a shared bus
Interconnection network:
n x n multistage switch built from smaller-sized switches
fragment datagram into fixed length cells
switch cells through the fabric, reassemble datagram at exit
Transfer packet from input link to appropriate output link
Switching rate: rate at which packets can be transfer from inputs to outputs
  Often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate R
Three major types of switching fabrics:
high-speed
switching
fabric
N input
ports
N output
ports
. . .
. . .
R
R
R
R
(rate: NR, ideally)
Memory
Traditional computers with switching under direct control of CPU

## Slide 5: Input Port Functions
line
termination
lookup,
forwarding
queueing
Decentralized switching:
Using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
Destination-based forwarding: forward based only on destination IP address (traditional)
Generalized forwarding: forward based on any set of header field values
Physical layer:
Decode the optical /electrical signal into 1s and 0s
switch
fabric
link
layer
protocol
(receive)
Link layer:
E.g., Ethernet
Perform link-layer operations (next week)

## Slide 6: Output Port Queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate
Drop policy: drop datagrams if no free buffers
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Scheduling policies: performance vs. network neutrality
First come, first served
Priority
Round Robin
Weighted fair queueing, etc.
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
Notes: Not required:
Priority scheduling:
Arriving traffic is classified into multiple queues
Any header fields can be used for classification
send packet from highest priority queue that has buffered packets (FCFS within priority class)
Round Robin (RR) scheduling:
Classify arriving traffic and put them into multiple queues
Router cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
Weighted Fair Queuing (WFQ):
Classify arriving traffic and put them into multiple queues
Assign each queue a weight
Each class, i, has weight, wi, and gets weighted amount of service in each cycle: wi / Sum(wj)

## Slide 7
Forwarding Pipeline
When a packet arrives, what does the input linecard need to do?
Input port: Receive signals and assemble data packets
Process the packet:
  Parse the packet to understand its headers, e.g. IPv4 or IPv6
  Look up the next hop in the forwarding table
  Update the packet: Decrement TTL, update checksum, fragment packet if it's too big, etc.
Send the packet onwards:
  Fabric interconnect chip sends packets to other linecards via inter-chassis links
Linecard
CPU
Forwarding Chip
Forwarding Chip
Fabric Chip(s)
To Fabric
Fabric
PHY
MAC
Parse
Lookup
Actions
Fabric Interconnect
To other linecards
Hardware
Forwarding Chip
Fabric Chip
Queuing
Notes: For a router, how does it know which output port to send an incoming packet to?

## Slide 8: Efficient Forwarding
The forwarding table is a map (key-value pairs)
How do we do fast lookups?
Challenges:
Entries can contain a range of addresses, not just one
Ranges might overlap; A destination can match multiple entries. E.g., output port 5 connects to hosts in 2.1.1.0/24
Naive solution: Write out the whole range:
Table gets really big
If a route changes, we have to update tons of entries. E.g., 2.1.1.0/24 connects to port 6?
We need something smarter
R2's Table | 
Destination | Port
2.1.1.0/24 | 5
R2's Table | 
Destination | Port
2.1.1.0 | 5
2.1.1.1 | 5
2.1.1.2 | 5
2.1.1.3 | 5
2.1.1.4 | 5
... | ...
2.1.1.252 | 5
2.1.1.253 | 5
2.1.1.254 | 5
2.1.1.255 | 5

## Slide 9: Destination-based Forwarding
Q: What happens if ranges don’t divide up so nicely? E.g., packets with a destination address within a subset in this first range should go to interface 3?
3
Maps destination IP address ranges to specific output link interfaces in a router
Router checks the destination address of each incoming packet and uses the table to determine which link interface to forward the packet to
A: Split the first address range into multiple pieces and add new entries. Or a more elegant way: longest prefix matching
Notes: "Destination-based forwarding" refers to the process of using a forwarding table that maps destination IP address ranges to specific output link interfaces in a router. The router checks the destination address of each incoming packet and uses the table to determine which link interface to forward the packet to.
Let’s now consider the “simplest” case that the output port to which an incoming packet is to be switched is based on the packet’s destination address:
1. A brute-force implementation of the forwarding table would have one entry for every possible destination address. Since there are more than 4 billion possible addresses, this option is totally out of the question.
2. As an example of how this issue of scale can be handled, let’s suppose that our router has four links, numbered 0 through 3, and that packets are to be forwarded to the link interfaces as above table.
The question refers to the situation where the destination address ranges in a forwarding table don't align perfectly into clean, non-overlapping ranges. This could occur when IP address ranges overlap, or when subnets don't fit neatly into fixed-length ranges.
In such cases, it becomes more difficult to decide which interface to forward the packet to because a packet might match multiple ranges, leading to ambiguity or additional processing to determine the most specific match. In networking, this is often handled by the longest prefix match rule, where the forwarding decision is based on the range with the longest matching bits (most specific match) between the destination IP address and the entries in the forwarding table.

## Slide 10: Longest Prefix Matching
We want a fast implementation of longest prefix matching
Instead of using explicit ranges, use longest address prefix that matches destination address
If the address matches multiple prefixes, take the most specific (longest) match
If the address matches no prefixes, take the default route
If there's no default route, drop the packet.
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 11: Longest Prefix Matching
Instead of using explicit ranges, use longest address prefix that matches destination address
If the address matches multiple prefixes, take the most specific (longest) match
If the address matches no prefixes, take the default route
If there's no default route, drop the packet.
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 12: Longest Prefix Matching
Instead of using explicit ranges, use longest address prefix that matches destination address
If the address matches multiple prefixes, take the most specific (longest) match
If the address matches no prefixes, take the default route
If there's no default route, drop the packet.
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 13: Longest Prefix Matching
Instead of using explicit ranges, use longest address prefix that matches destination address
If the address matches multiple prefixes, take the most specific (longest) match
If the address matches no prefixes, take the default route
If there's no default route, drop the packet.
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 14: Efficient Longest Prefix Matching with Tries
Is there a map data structure that supports efficient longest prefix match?
We can use a more obscure data structure: Tries
Idea: Spell out each key, one letter/digit at a time
A node is marked blue if walking from root to that node forms a valid key
Longest prefix matching on a trie:
Start at the root, and spell out the word
Remember most recent (longest) key you see along the way
Stop when you're done, or fall off the tree. Return the longest key you saw
If you finish spelling or fall off the tree without seeing any other prefix, the default is returned
...
0..
1..
00.
001
Key | Value
... | 0
0.. | 1
100 | 2
101 | 3
001 | 4
10.
100
101
4
2
3
1
Longest prefix of 00100 is 001  Port 4
Longest prefix of 10000 is 100  Port 2
Longest prefix of 11100 is default  Port 0
0

## Slide 15
Roadmap
Packet Forwarding
Define the Routing Problem
Routing Protocol: Link State

## Slide 16: Modeling the Network
We'll draw the network as a graph:
Each node represents a machine
Each edge represents a link. For now, assume every link is undirected and connects exactly 2 machines
Assume each machine is identified by a unique label (e.g., IP addr)
A
R1
R7
R5
C
R6
D
R2
R3
R4
R8
B
A
R1
= End host
= Router
Two types of machines on the network (simplified):
End hosts send and receive packets, to and from other end hosts.
Example: Your personal computer
End hosts don't forward intermediate packets.
Routers forward intermediate packets
Example: Your home router, heavy-duty router in a datacenter
For now, assume routers don't send and receive packets of their own

## Slide 17: Modeling the Network
Packets are the basic unit of data sent across the network.
Packets have a header with metadata
For now, we only care about the source address and destination address fields
Packets have a payload with the application data
Example: Website contents, image, etc.
Routing isn't concerned about the payload. It's just some sequence of 1s and 0s we have to forward
Source Address
Destination Address
Payload

## Slide 18
Least-Cost Routing
What makes a routing solution good? Many different ways to define good, including:
Transmission delay
Price cost
Unreliability
Bandwidth constraints
Least-cost routing: Assign costs to every edge, and find paths with lowest cost
Cost depends on the metric the operator wants to minimize.
Costs can be arbitrary. Routing protocols don't care where the costs come from.
A
R1
R7
R5
C
R6
D
R2
R3
R4
R8
B
1
2
2
10
1
1
1
2
2
2
1
1
1

## Slide 19
In least-cost routing, routers should forward packets such that they take the lowest-cost path to the destination
Example: If all costs are 1, the protocol finds paths with the fewest hops
Usually, if edges are unlabeled, assume they have cost 1
A
1
R3
R2
R1
R5
R4
1
1
1
7
2
1
10
A
1
R3
R2
R1
R5
R4
B
1
1
1
7
2
1
10
B
A → B Cost = 7
A → B Cost = 14
Least-Cost Routing

## Slide 20
Where do costs come from?
Costs are local to a router. Each router knows the cost of its own links
In practice, generally configured by an operator
Properties of costs:
Costs are always positive integers
  Consistent with almost any practical metric you'd use: bandwidth, delay, etc.
Usually, costs are symmetrical
  A → B costs the same as B → A
  Exceptions possible in theory (e.g. different upload/download bandwidth)
These two assumptions will simplify our routing protocols
Least-Cost Routing

## Slide 21
Routing vs. Forwarding
Forwarding:
Look up packet's destination in table, and send packet to neighbor.
Inherently local. Depends only on arriving packet and local table.
Occurs every time a packet arrives (nanoseconds)
Routing:
Communicates with other routers to determine how to populate tables
Inherently global: Must know about all destinations, not just local ones
Occurs every time the network changes (e.g. a link fails)
To: B
R2
R2's Table | 
Destination | Port
A | 0
B | 1
C | 1
D | 2
1
2
0
Forwarding is local
R2
R1
A
R3
R4
B
C
D
0
1
2
Routing is global
Not local!

## Slide 22
Roadmap
Packet Forwarding
Define the Routing Problem
Routing Protocol: Link State

## Slide 23
Routing Protocols: Roadmap
Routing protocols can be classified by:
Where they operate:
  Intra-domain: routing packets within a local network
  Inter-domain: routing packets across different networks
How they operate (Distance-vector, link-state, or path-vector)
Today, we'll look at link-state protocols
Major examples:
  IS-IS (Intermediate System to Intermediate System)
  OSPF (Open Shortest Path First)
 | Intra-domain (Interior Gateway Protocol) | Inter-domain (Exterior Gateway Protocol)
Distance-vector | Routing Information Protocol (RIP) | –
Link-state | IS-IS, OSPF | –
Path-vector | – | BGP
Notes: The protocols for routing packets within a local network are called intra-domain routing protocols, or interior gateway protocols (IGPs). Real-world examples include OSPF (Open Shortest Path First) and IS-IS (Intermediate System to Intermediate System).
The protocols for routing packets across different networks are called inter-domain routing protocols, or exterior gateway protocols (EGPs). In order to support sending packets across different local networks, every network needs to agree to use the same protocol for routing packets between each other.

## Slide 24
Link-State Protocols: Definition
Link-state protocols:
Every router learns the full network graph.
Then, each router runs a shortest-path algorithm on the graph to populate the forwarding table.
Distance-vector:
Local data: Each node only knows about part of the network.
Global (distributed) computation: Each node computes part of the solution, working with other nodes.
Link-state:
Global data: Each node knows about the full network graph.
Local computation: Each node computes the full solution by itself.
How do routers learn this?
What algorithm do we run?

## Slide 25
Suppose R3 has learned the full network graph
We know all the links, their status (up or down?), and their costs
We know about all the destinations
R3 can run a graph algorithm to compute paths
We can populate the forwarding table with the next-hop (in the computed path)
Link-State Protocols: Definition
How do routers learn this?
What algorithm do we run?
R3
R2
R1
R5
R4
1
1
1
7
2
1
10
A
B
1
R3's Table | 
Destination | Next Hop
A | R2
... | ...

## Slide 26
What graph algorithm do we run to compute paths?
Any single source shortest-path algorithm will work
Need to find shortest paths from a single source (the router) to every host
Some possible choices:
Bellman-Ford (the original serial version)
Dijkstra's algorithm
Breadth-first search
Parallel single-source shortest path
Dynamic shortest path
Approximate shortest path
etc.
Link-State Algorithms
R3
R2
R1
R5
R4
1
1
1
7
2
1
10
A
B
1
R3's Table | 
Destination | Next Hop
A | R2
... | ...

## Slide 27
Steps of Learning Network Graph
Link-state protocols:
Every router learns the full network graph
  Step 1A: Discover my neighbors
  Step 1B: Tell everybody about my neighbors
Then, each router runs a shortest-path algorithm on the graph to populate the forwarding table
How do routers learn this?

## Slide 28
Steps of Learning Network Graph (1/2): Learn Neighbors
How do we discover who is adjacent to us and their identity? Say hello!
Routers periodically send hello messages to their neighbors.
If they stop saying hello, assume that they disappeared.
This helps us learn about our direct neighbors, but not the whole network.
  R1 does not know about the rest of the network (e.g. R3).
R1
R2
R3
Hello, I'm R2.
Hello, I'm R2.
Hello, I'm R1.
Hello, I'm R3.
My neighbor is R2.
My neighbor is R2.
My neighbors are R1 and R3.

## Slide 29
Steps of Learning Network Graph (2/2): Propagate Neighbor Information
How do we learn about the rest of the network, beyond our neighbors?
Solution: Flood information across the network.
When local information changes, send it to everyone.
When you receive information from your neighbor, send it to everyone.
R1
R1 and R2 are neighbors. Tell everyone!
R1 and R2 are neighbors. Tell everyone!
R2
R1 and R2 are neighbors. Tell everyone!
R3

## Slide 30
Steps of Learning Network Graph
Link-state protocols:
Every router learns the full network graph
  Step 1A: Discover my neighbors
  Step 1B: Tell everybody about my neighbors
Then, each router runs a shortest-path algorithm on the graph to populate the forwarding table

## Slide 31: Dijkstra’s Shortest Path Algorithm
Centralized: network topology, link costs known to all nodes
  Accomplished via “link state broadcast”
  All nodes have same info
Computes least cost paths from one node (“source”) to all other nodes
  Gives forwarding table for that node
Iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
notation

## Slide 32: Dijkstra’s Shortest Path Algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find a node w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 33: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
Initialization (step 0):
For all a: if a adjacent to u then D(a) = cu,a

## Slide 34: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 35: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
∞
2,x
4,x
2,u
D(v) = min ( D(v), D(x) + cx,v ) = min(2, 1+2) = 2
D(w) = min ( D(w), D(x) + cx,w ) = min (5, 1+3) = 4
D(y) = min ( D(y), D(x) + cx,y ) = min(inf,1+1) = 2

## Slide 36: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy

## Slide 37: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
4,y
3,y
2,u
D(w) = min ( D(w), D(y) + cy,w ) = min (4, 2+1) = 3
D(z) = min ( D(z), D(y) + cy,z ) = min(inf,2+2) = 4

## Slide 38: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv

## Slide 39: Dijkstra’s Algorithm: an Example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(w) = min ( D(w), D(v) + cv,w ) = min (3, 2+3) = 3
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y

## Slide 40: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw

## Slide 41: Dijkstra’s Algorithm: an Example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(z) = min ( D(z), D(w) + cw,z ) = min (4, 3+5) = 4
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y

## Slide 42: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz

## Slide 43: Dijkstra’s Algorithm: an Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )

## Slide 44: Dijkstra’s Algorithm: an Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 45: Dijkstra’s Algorithm: Discussion
Algorithm complexity: n nodes
Each of n iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2) complexity
More efficient implementations possible: O(nlogn)
Message complexity:
Each router must broadcast its link state information to other n routers
Efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
Each router’s message crosses O(n) links: overall message complexity: O(n2)