## Slide 1: CSC 3511 Security and Networking
Week 6, Lecture 2: Link Layer

## Slide 2
Roadmap
Link Layer and LAN
Multiple Access Protocol
Sending Ethernet Packets

## Slide 3: Link Layer: Introduction
Link layer has responsibility of transferring data between adjacent nodes over a single link
Scope: One "hop" at a time (node-to-node, same local network)
Different from Network Layer: Link layer  one hop, Network layer  end-to-end path
Link Layer Terminology
Frame: Link layer packet (encapsulates network layer datagram)
Links: Physical communication channels connecting physically adjacent nodes. E.g., Wired (fiber optical cable, copper cable) or wireless (WiFi channel, cellular)
Nodes: Host, routers
Different links use different protocols:
WiFi on first hop → Ethernet on next hop → …
Same datagram, different link-layer protocols at each hop
mobile network
enterprise
network
national or global ISP
datacenter
network

## Slide 4: Transportation analogy
Transportation analogy:
Travel agent = routing algorithm
  Determines the overall path and which modes to use
Trip from San Jose, CA to Milwaukee, WI
  Uber: San Jose to SFO
  Plane: SFO to ORD
  Train: ORD to Milwaukee
Passenger = frame
  The "packet" being transported
Transport segment = communication link
  The physical path/medium
Transportation mode = link-layer protocol
  Different rules/methods for each segment
  E.g., Uber – road protocol; Airline – air protocol; Amtrak – rail protocol
San Jose, CA
SFO
ORD
Milwaukee, WI
Notes: Consider a travel agent who is planning a trip for a tourist traveling from San Jose CA, to Milwaukee, WI.
The travel agent decides that it is most convenient for the tourist to take an Uber from San Jose to SFO airport, then a plane from SFO airport to Chicago’s airport, and finally a train from ORD airport to Milwaukee’s train station.
Once the travel agent makes the three reservations:
It is the responsibility of the Uber to get the tourist from San Jose to SFO;
It is the responsibility of the airline company to get the tourist from SFO to ORD;
It is the responsibility of the Amtrak train service to get the tourist from Chicago to Milwaukee.
Each of the three segments of the trip is “direct” between two “adjacent” locations. Note that the three transportation segments are managed by different companies and use entirely different transportation modes (car, plane, and train).
Although the transportation modes are different, they each provide the basic service of moving passengers from one location to an adjacent location. In this transportation analogy, the tourist is a frame, each transportation segment is a link, the transportation mode is a link layer protocol, and the travel agent is a routing protocol.

## Slide 5: Link layer: Services
Framing, link access:
  Encapsulate datagram into frame, adding header, trailer
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
  Channel access if shared medium
Reliable delivery between adjacent nodes
  Unnecessary, mostly used on high bit-error links (wireless) where data corruption or loss is more frequent
  Correct errors locally
…
…
Cable access
cellular
WiFi
Ethernet LANs
Q: why both link-level and end-end reliability?
Link layer errors do not propagate further, more efficient than end-to-end retransmission
An additional layer of error checking and correction
Notes: Framing: A frame consists of a data field, in which the network-layer datagram is inserted, and a number of header fields. The structure of the frame is specified by the link-layer protocol.
Link access: A medium access control (MAC) protocol specifies the rules by which a frame is transmitted onto the link. For point-to-point links that have a single sender at one end of the link and a single receiver at the other end of the link, the MAC protocol is simple. The sender can send a frame whenever the link is idle. The more interesting case is when multiple nodes share a single broadcast link: the so-called multiple access problem. Here, the MAC protocol serves to coordinate the frame transmissions of the many nodes.
Reliable delivery: When a link-layer protocol provides reliable delivery service, it guarantees to move each network-layer datagram across the link without error. Recall that certain transport-layer protocols (such as TCP) also provide a reliable delivery service. A link-layer reliable delivery service is often used for links that are prone to high error rates, such as a wireless link, with the goal of correcting an error locally (on the link where the error occurs) rather than forcing an end-to-end retransmission of the data. However, link-layer reliable delivery can be considered an unnecessary overhead for low bit-error links, including fiber, coax, and many twisted-pair copper links. For this reason, many wired link-layer protocols do not provide a reliable delivery service.
A:
Link-Level Reliability ensures reliable data transfer between two adjacent nodes on the same link (e.g., between a device and a router or between two routers). It detects and retransmits corrupted frames, ensuring that errors introduced at the link level (due to noise, interference, or congestion) do not propagate further. This keeps the network efficient by correcting errors locally without involving the end systems for every minor issue. Keywords: performance and efficiency
It provides the ultimate assurance that data arrives safely from source to destination, which is particularly important for applications like file transfer or video streaming. keywords: robust communication, an additional layer of error checking and correction

## Slide 6: Link Layer: Services
Flow control:
  Pacing between adjacent sending and receiving nodes
Error detection:
  Errors caused by signal attenuation, noise.
  Receiver detects errors, signals retransmission, or drops frame
Error correction:
  Receiver identifies and corrects bit error(s) without retransmission
Half-duplex and full-duplex:
  With half duplex, nodes at both ends of link can transmit (two-way transmission), but not at same time
…
…
Cable access
cellular
WiFi
Ethernet LANs
Notes: Error detection and correction. The link-layer hardware in a receiving node can incorrectly decide that a bit in a frame is zero when it was transmitted as a one, and vice versa. Such bit errors are introduced by signal attenuation and electromagnetic noise. Because there is no need to forward a datagram that has an error, many link-layer protocols provide a mechanism to detect such bit errors. This is done by having the transmitting node include error-detection bits in the frame, and having the receiving node perform an error check. Recall that the Internet’s transport layer and network layer also provide a limited form of error detection—the Internet checksum. Error detection in the link layer is usually more sophisticated and is implemented in hardware. Error correction is similar to error detection, except that a receiver not only detects when bit errors have occurred in the frame but also determines exactly where in the frame the errors have occurred (and then corrects these errors).
Error correction is similar to error detection, except that a receiver not only detects when bit errors have occurred in the frame but also deter- mines exactly where in the frame the errors have occurred (and then corrects these errors).

## Slide 7: Host Link Layer Implementation
In each-and-every host
Link layer implemented on-chip or in network interface card (NIC) (aka, network adapter)
  Implements link and physical layer
Attaches into host’s system buses
Combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical
Notes: The Ethernet capabilities are either integrated into the motherboard chipset or implemented via a low-cost dedicated Ethernet chip. For the most part, the link layer is implemented on a chip called the network adapter, also sometimes known as a network interface controller (NIC). The network adapter implements many link layer services including framing, link access, error detection, and so on.

## Slide 8: Interfaces Communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
Sending side:
Encapsulates datagram in frame
Adds error checking bits, reliable data transfer, flow control, etc.
Receiving side:
Looks for errors, reliable data transfer, flow control, etc.
Extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 9
Roadmap
Link Layer and LAN
Multiple Access Protocol
Sending Ethernet Packets

## Slide 10
Connecting Local Hosts
A
B
D
E
C
A
B
C
D
E
Option 1: Point-to-point links
Every pair of hosts has a dedicated link
Expensive cabling and ports, does not scale:
  For N hosts, need N(N-1)/2 links
  For every new host, we have to add new links to every other host
  Need a lot of (physical) ports per host
Option 2: Shared Medium (Boradcase link, bus Topology)
A single wire can connect multiple computers. From the wire‘s perspective, the router is just a machine like any other.
All hosts connect to a single shared wire:
  Just one cable - easy to add new hosts
  Each host needs only 1 interface
Introduces a new problem - shared media:
  All hosts share the same communication channel
  What if A and B transmit at the same time? → COLLISION!
  Signals interfere, data corrupted
Challenge: Building a Local Network
Multiple hosts need to communicate in the same local area (e.g., office, home, campus building)
Q: How do we physically connect them?

## Slide 11
Shared Media and Multiple Access Protocols
Shared media:
If multiple machines transmit at the same time, signals will interfere or collide
Analogy: People talking simultaneously on a group call
Note: Shared media is not necessarily a wire
Could be light signals on a shared optical fiber
Or radio waves on a shared wireless link
A
B
C
D
E
Blah blah
Blah blah
??!
??!
??!
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: WiFi
shared wire (e.g.,
cabled Ethernet)
shared radio: 4G/5G
Q: How can multiple nodes share one channel without collisions?
A: Multiple Access Protocol  allocates the shared media to everyone wanting to use it

## Slide 12
Multiple Access Protocols (1/3) - Multiplexing
A multiple access protocol allocates the shared media to everyone wanting to use it
3 types of approaches
Several protocols of each type
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Time
Frequency
Multiplexing( aka Channel partitioning):
Divide channel into smaller “pieces” (time slots, frequency, code)
Allocate piece to node to each node for exclusive use
Time-based multiplexing: Give each node some fixed time slots
Frequency-based multiplexing: Divide medium into frequency channels

## Slide 13
TDMA: time division multiple access
Access to channel in “rounds”
Each node gets fixed length slot (length = packet transmission time) in each round
Unused slots go idle
Example: 6-node LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame
Multiple Access Protocols (1/3) - Multiplexing

## Slide 14
FDMA: frequency division multiple access
Channel spectrum divided into frequency bands
Each node assigned fixed frequency band
Unused transmission time in frequency bands go idle
Example: 6-node LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable
Multiple Access Protocols (1/3) - Multiplexing

## Slide 15
Multiple Access Protocols (1/3) - Multiplexing
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Time
Frequency
Idea: Allocate a fixed slice of resources to each node
Problem: Can be wasteful.
There's only so much frequency/time available to allocate
If a node has nothing to say, some frequency/time goes unused

## Slide 16
Multiple Access Protocols (2/3) – Taking Turns
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Time
Frequency
Taking turns:
Nodes take turns speaking
Polling protocols: A coordinator decides when each node can speak
  Example: Bluetooth
Token passing: Pass a virtual token around. Only the node with the token can speak
  Example: IBM Token Ring, FDDI

## Slide 17
Multiple Access Protocols (2/3) – Taking Turns
Polling protocols: A coordinator decides when each node can speak
A
B
C
D
Coordinator
A, do you have something to say?
Yes, blah blah blah
A can speak for as long as it needs
A
B
C
D
Coordinator
B, do you have something to say?
No
B has nothing to say
Coordinator can immediately move on to C

## Slide 18
Multiple Access Protocols (2/3) – Taking Turns
Token passing: Pass a virtual token around. Only the node with the token can speak
A
B
C
D
Blah blah blah
A holds the token.
A can speak for as long as it needs.
When A is done, it passes the token to B.
A
B
C
D
B has nothing to say.
It can immediately pass the token to C.
Token
Token

## Slide 19
Multiple Access Protocols (2/3) – Taking Turns
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Time
Frequency
Idea: Nodes take turns speaking
Benefit: No more time wasted on idling
  If someone has nothing to say, immediately move on
Problem: Complexity
  Need to implement inter-node communication
  How do we elect the central coordinator?
  What if two nodes both think they have the token?

## Slide 20
Multiple Access Protocols (3/3) – Random Access
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Time
Frequency
ALOHA random access scheme: "rude" version
If you have a packet, just send it
  Recipient replies with an ack
If two nodes send simultaneously, collision corrupts the packets.
  No ack!
If you don't get an ack: Wait some random amount of time, then resend.
  Randomness helps avoid another collision.

## Slide 21
Multiple Access Protocols (3/3) – Random Access
CSMA (Carrier Sense Multiple Access): "polite" version
Listen before transmit:
  If channel sensed idle: transmit entire frame
  If channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
Collision can still occur with carrier sensing:
Propagation delay means two nodes may not hear each other’s just-started transmission
Collision: entire packet transmission time wasted
  Distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 22
Multiple Access Protocols (3/3) – Random Access
CSMA/CD (Carrier Sense Multiple Access with Collision Detection):
Listen before sending, but also while you're sending
If you hear someone else sending, stop! Collision detected!
CSMA/CD uses binary exponential backoff:
After every collision, wait up to twice as long before resending.
  After first collision: Wait between 0–4 seconds.
  If resend collides again: Wait between 0–8 seconds.
Resends fast when possible, slowing down when necessary (e.g. many senders)
spatial layout of nodes

## Slide 23: Ethernet CSMA/CD Algorithm
Ethernet receives datagram from network layer, creates frame
If Ethernet senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If entire frame transmitted without collision - done!
If another transmission detected while sending: abort, send jam signal
After aborting, enter binary (exponential) backoff:
  after mth collision, chooses K at random from {0,1,2, …, 2m-1}. Ethernet waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maximum value that n can take is capped at 10.

## Slide 24
Roadmap
Link Layer and LAN
Multiple Access Protocol
Sending Ethernet Packets

## Slide 25
Ethernet as LAN Network Protocol
Local Area Networks (LANs) are typically Ethernet
Machines in the same LAN can exchange messages directly at Layer 2!
  No need for IPs, routers, forwarding, etc.
  Use MAC addresses instead
Analogy: If we're in the same office building
  Same floor (LAN): Walk directly to colleague's desk  Layer 2 (Ethernet)
  Different buildings (different networks): Need address & postal system  Layer 3 (IP routing)

## Slide 26
Ethernet Addressing
At layer 2, each machine has a MAC address (Media Access Control)
Function: used “locally” to get frame from one interface to another physically-connected interface (same subnet)
48 bits, written in hex, e.g. f8:ff:c2:2b:36:16
Stored permanently on the machine ("burned in")
  Often can be overridden by software
Allocated according to organization, e.g. manufacturer of the machine
Globally unique. You might plug your computer in anywhere
00
0111111111111101000011
110101000110110001101000
2 bits of flags
22-bit manufacturer ID, assigned by IEEE
24-bit machine ID,
assigned by vendor
  Vendors Get OUIs (Organizationally Unique Identifier, the first 24 bits) with first bit = 0, e.g., 00:1A:2B:xx:xx:xx
  Manufacturer fills in the last 24 bits (xx:xx:xx) for each device
Beware of endianness
Notes: Understanding bit transmission order in Ethernet
For example, an address in canonical form 12-34-56-78-9A-BC:
1. Standard logical view:
12 (hex) = 0001 0010 (binary)
34 = 0011 0100
56 = 0101 0110
78 = 0111 1000
9A = 1001 1010
BC = 1011 1100
2. Ethernet transmits each byte with the LSB (Least Significant Bit) first. So each byte gets bit-reversed during transmission:
0001 0010 → reversed → 0100 1000
0011 0100 → reversed → 0010 1100
0101 0110 → reversed → 0110 1010
0111 1000 → reversed → 0001 1110
1001 1010 → reversed → 0101 1001
1011 1100 → reversed → 0011 1101
3. Actual transmitted sequence:
01001000 00101100 01101010 00011110 01011001 00111101

## Slide 27
Types of LAN Communication
Ethernet supports three types of communication:
Unicast: Send a packet to a single recipient
Broadcast: Send a packet to everyone on the local network
Multicast: Send a packet to everyone in a specific group
  Machines in the local network can join groups
Unicast: Send a packet to a single recipient
Destination = the recipient's MAC address
Recall: On a shared medium, everybody gets the signal
When you get a packet, check the destination to see if it's meant for you
If not, ignore the packet
Broadcast: Send a packet to everyone on the local network
Packet already reaches everybody on the shared medium
  We just need to make sure everyone knows it's meant for them
Destination = the broadcast address, FF:FF:FF:FF:FF:FF

## Slide 28
Types of LAN Communication
Multicast: Send a packet to everyone in a specific group
How group addresses work:
  These are used by software/protocols, not burned into hardware
  First bit = 1  reserved for multicast/group address, e.g., 01:00:5E:xx:xx:xx = IPv4 multicast
  When a device wants to join a multicast group, it configures its NIC to listen for that group address
A device can listen to multiple multicast addresses, but its burned-in address is always unicast
Broadcast is just a special case of multicast, where everyone is in a group
10
0111111111111101000011
110101000110110001101000
If this bit is 1, it's a group address
Example of using multicast: Bonjour/mDNS
Invented by Apple.
All Apple products join a multicast group.
Apple devices can multicast to the group.
  iPhone says: "Hey, local Apple products, can anyone play music?“
  Apple TV says: "Hey, local Apple products, I'm an Apple TV."

## Slide 29
Ethernet Packet Structure
A data packet in Ethernet (IEEE 802.3) is often called a frame.
Many fields (destination, source, type, checksum) similar to IP header
Need additional fields to separate packets on the wire
Preamble (7 bytes)
SFD (1)
Destination MAC (6)
Source MAC (6)
length (2)
Payload
FCS (4)
IPG (12)
Signal start of new packet on wire
Destination
length of the entire Ethernet frame (MTU 1500 bytes)
Source
Signal end of packet on wire
Checksum