## Slide 1: CSC 3511 Security and Networking
Week 7, Lecture 2: Link Layer

## Slide 2
Roadmap
Error Detection and CRC
Synthesis: A Day in the Life of a Web Request

## Slide 3: Error Detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  Protocol may miss some errors, but rarely
  Larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 4: Checksum (Review, see W3D2 UDP)
Sender (UDP):
Prepare the UDP packet
  Header: source & destination port, checksum (initialized as 0)
  Data: The actual payload
Create the pseudo-header
  Source IP, destination IP, protocol number (17 for UDP), total length (header & data)
Compute & insert checksum
  A special case: if the computed checksum is zero; it’s transmitted as 0xFFFF
Receiver (UDP):
Receive the UDP packet
Rebuild the pseudo-header
Verify checksum of received segment:
  Add everything together, verify if the result is all 1s (1111 1111 1111 1111)
  Not all 1s  Error detected
  All 1s  No error detected. But maybe errors nonetheless? More later ….
Goal: Detect errors (i.e., flipped bits) in transmitted datagrams/segments

## Slide 5: Parity Checking
Single bit parity:
Add one extra bit to make the total number of 1s either even or odd
Detect single bit errors
0111000110101011
1
(even) parity bit
d (16) data bits, nine 1s
Two-dimensional parity:
Detect and correct single bit errors (without retransmission!)
See the even parity example below
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
no errors:
parity
error
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
0 0 1 0 1 0
detected
and
correctable
single-bit
error:
Even parity:
Total number of 1s (including the parity bit) should be even
Odd parity:
Total number of 1s (including the parity bit) should be odd
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/2d_parity.php
At receiver:
Compute parity of d received bits
Compare with received parity bit – if different than error detected
Notes: The bottom-right corner bit IS required and serves an important purpose: This is a check bit for the parity bits themselves!
Three equivalent methods (all give same result):
Method 1: Parity of all row parity bits  Calculate even parity of the rightmost column (all row parity bits)
Method 2: Parity of all column parity bits  Calculate even parity of the bottom row (all column parity bits)
Method 3: Parity of ALL data bits  Calculate even parity of the entire data matrix
Without the corner bit, you can't distinguish certain error patterns, such as an error in a parity bit itself.
E.g.,: 10101|0 ← ERROR HERE (should be 1)
11110|0
01110|1
------+-
00101|?(0)
Without corner bit: Can't tell if error is in data or parity bit!

## Slide 6: Cyclic Redundancy Check (CRC)
More powerful error-detection coding
Treat data as a polynomial, divide by a generator polynomial (G), use remainder as checksum
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given, specified in CRC standard)
Sender: compute r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  Receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  Can detect all burst errors less than r+1 bits
  Widely used in practice (Ethernet, 802.11 WiFi)
<D,R> = D 2r XOR R
*
formula for these bits
r CRC bits
d data bits
D
R
bits to send

## Slide 7: Cyclic Redundancy Check (CRC): Example
Sender wants to compute R, such that:
  D . 2r XOR R = nG
Check out the online interactive exercises for more examples:
http://gaia.cs.umass.edu/kurose_ross/interactive/CRC.php
D.2r
G
R = remainder [ ]
... or equivalently (XOR R both sides):
  D . 2r = nG XOR R
... which says:
if we divide D . 2r by G, we want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r (here, r=3)
*
1
0
1
algorithm for
computing R
CRC uses
modulo-2 division (XOR)
Generator polynomial: x³ + 1 → Binary: 1001 (4 bits)
Data to send: 101110 (6 bits)
Step 1: Append 3 zeros to data (degree of generator = 3)
Notes: What CRC does:
Detects errors very reliably (can detect burst errors, bit flips)
Cannot fix errors: Only tells you "this frame is corrupted“
Action on error: Discard the frame
Error Correction Schemes in Link Layer
Wi-Fi (802.11): LDPC (Low-Density Parity-Check) codes (802.11n/ac/ax)
Cellular Networks (4G/5G): Turbo codes (4G LTE), LDPC codes (5G)
Satellite Communications: Reed-Solomon codes
Reference: https://en.wikipedia.org/wiki/Error_correction_code

## Slide 8
Roadmap
Error Detection and CRC
Synthesis: A Day in the Life of a Web Request

## Slide 9: Synthesis: A Day in the Life of a Web Request
Our journey down the protocol stack is now complete!
  Application, transport, network, link
Putting-it-all-together: synthesis!
  Goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  Scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 10: A Day in the Life: Scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
Arriving mobile client attaches to network …
Requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 11: A Day in the Life: Connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
Connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-muxed to IP de-muxed, UDP de-muxed to DHCP

## Slide 12: A Day in the Life: Connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP Offer containing client’s IP address, subnet mask, IP address of first-hop router (default gateway), name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
Encapsulation at DHCP server, DHCP Offer frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, subnet mask, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 13: A Day in the Life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
Before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
Client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 14: A Day in the Life… Using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
de-muxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 15: A Day in the Life…TCP Connection Carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
To send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
Client responds with ACK; TCP connection established! (step 3)
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
Web server responds with TCP SYN-ACK (step 2 in TCP 3-way handshake)

## Slide 16: A Day in the Life… HTTP Request/Reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
Web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed