## Slide 1: CSC 3511 Security and Networking
Week 2, Lecture 1: Network Structure

## Slide 2: Roadmap
Review: What is the Internet? What is a protocol?
Network structure: how to build a “network of networks”
Layers and encapsulation/decapsulation
Notes: Bandwidth: capacity
Latency: delay
Loss: dropped packets
Jitter: variation in delay

## Slide 3: What’s the “Internet”?
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches:
forward packets (chunks of data) as “network core”
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps as “network edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 4: What’s a protocol – A Human Analogy
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Protocols define the format, order of messages sent and received among network
entities, and actions taken on message transmission, receipt
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Notes: Important points:
Distributed entities, exchanging messages (governed by protocols)
Time going down
How to define a protocol? (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 5: Roadmap
Review: What is the Internet? What is a protocol?
Network structure: how to build a “network of networks”
Layers and encapsulation/decapsulation
Notes: Bandwidth: capacity
Latency: delay
Loss: dropped packets
Jitter: variation in delay

## Slide 6: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge (endpoint):
Personal computers (PCs), adapters, modems, and devices that connect to them

## Slide 7: A closer look at Internet structure
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 8: Two key network-core functions
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
local forwarding table
Forwarding:
aka “switching”
Local action: move arriving packets from router’s input link to appropriate router output link
local forwarding table
Routing:
Find paths through the network
Global action: determine source-destination paths taken by packets
routing algorithms
routing algorithm
Notes: End systems are connected by a packet-switched network
When one end system has data to send to another end system, the sending end system segments the data and adds header bytes to each segment. The resulting packages of information, known as packets in the jargon of computer networks, are then sent through the network to the destination end system, where they are reassembled into the original data.
A packet switch takes a packet arriving on one of its incoming communication links and forwards that packet on one of its outgoing communication links.

## Slide 9: Postal Analogy
routing
Imagine you‘re mailing a package from San Jose, CA to Northampton, MA
Routing is like GPS planning your entire trip before you start:
  Packages from California to Massachusetts should go through major sorting facilities in Denver, then Chicago, then finally to Massachusetts
  This is the path determination - done once, updated occasionally
  Need routing algorithm
traceroute command:
  PowerShell command:
    tracert google.com
    tracert 8.8.8.8
  Linux command: traceroute google.com
  Web-based tool: https://tools.keycdn.com/traceroute
Notes: Look at this map showing the route from San Jose to Northampton.
Routing is like GPS planning your entire trip before you start. The routing algorithm calculates: 'To get from San Jose to Northampton, take Highway 101 to I-80 East, then I-80 through Nevada and Utah, connect to I-76 in Colorado, then I-70 through Illinois...' This is the complete path computation - done once before the trip starts.
Forwarding is what you do at each highway intersection. When you reach Sacramento, you see the intersection signs. You check your next-hop instruction: 'Destination: Northampton... take I-80 East.' You don't recalculate the entire route - you just follow the sign for your next highway.
Now look at the Cleveland intersection closeup. The car arrives and needs a quick decision. The forwarding table at this intersection says:
Boston area → Take I-90 East
New York → Take I-80 East
Pittsburgh → Take I-76 West
That's it - a simple lookup. 'Northampton? That's Massachusetts, so I-90 East.'
In routers:
Routing builds the complete map and computes optimal paths between all destinations (happens every few seconds/minutes)
Forwarding is just reading the road signs at each intersection - matching destination to output port (happens billions of times per second)
A router's forwarding table is like having only the relevant highway signs for that specific intersection - just enough information to send packets to the next router. 8.8.8.8 is Google's Public DNS server. It's commonly used for Testing internet connectivity
Reading tracert output:
1 1 ms 1 ms 1 ms dsldevice.attlocal.net [192.168.1.254]
^ ^ ^ ^ ^ ^
| | | | | |
| | | | | └─ IP address
| | | | └─ Hostname (reverse DNS lookup)
| | | └─ 3rd probe packet round-trip time
| | └─ 2nd probe packet round-trip time
| └─ 1st probe packet round-trip time
└─ Hop number (TTL/distance from your computer)

## Slide 10: Postal Analogy
forwarding
forwarding
Imagine you‘re mailing a package from San Jose, CA to Northampton, MA
Forwarding is what you do at each highway intersection:
  When you reach Sacramento, you see the intersection signs. You check your next-hop instruction: “Destination: Northampton... take I-80 East”
  You don't recalculate the entire route  you just follow the sign for your next highway
  A simple look up  This happens at every stop: a quick, local decisions based on a simple lookup table
Notes: Look at this map showing the route from San Jose to Northampton.
Routing is like GPS planning your entire trip before you start. The routing algorithm calculates: 'To get from San Jose to Northampton, take Highway 101 to I-80 East, then I-80 through Nevada and Utah, connect to I-76 in Colorado, then I-70 through Illinois...' This is the complete path computation - done once before the trip starts.
Forwarding is what you do at each highway intersection. When you reach Sacramento, you see the intersection signs. You check your next-hop instruction: 'Destination: Northampton... take I-80 East.' You don't recalculate the entire route - you just follow the sign for your next highway.
Now look at the Cleveland intersection closeup. The car arrives and needs a quick decision. The forwarding table at this intersection says:
Boston area → Take I-90 East
New York → Take I-80 East
Pittsburgh → Take I-76 West
That's it - a simple lookup. 'Northampton? That's Massachusetts, so I-90 East.'
In routers:
Routing builds the complete map and computes optimal paths between all destinations (happens every few seconds/minutes)
Forwarding is just reading the road signs at each intersection - matching destination to output port (happens billions of times per second)
A router's forwarding table is like having only the relevant highway signs for that specific intersection - just enough information to send packets to the next router.

## Slide 11: Internet structure: a “network of networks”
Hosts connect to Internet via access Internet Service Providers (ISPs):
  Residential: AT&T, Spectrum, Verizon
  Mobile: T-Mobile, Verizon Wireless, AT&T Mobility
What is an ISP?
  What they do: Provide the physical connection + IP address assignment
  What you pay for: Bandwidth (50 Mbps, 1 Gbps), often with data caps
Access ISPs in turn must be interconnected
    So that any two hosts (anywhere!) can send packets to each other
Resulting network of networks is very complex
Let’s take a stepwise approach to describe current Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 12: Internet structure: a “network of networks”
Question: given millions of access Internet Service Providers (ISPs), how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 13: Internet structure: a “network of networks”
…
…
…
…
…
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 14: Internet structure: a “network of networks”
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 15: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….

## Slide 16: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. who will want to be connected
IXP
peering link
Internet exchange point: a direct interconnection of networks
IXP
Notes: An Internet Exchange Point (IXP) is a physical infrastructure through which different internet service providers (ISPs), content delivery networks (CDNs), and other network operators connect to exchange internet traffic. The primary purpose of an IXP is to facilitate the direct interconnection of networks, allowing them to exchange data traffic without needing to route that traffic through a third-party network.

## Slide 17: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP

## Slide 18: Internet structure: a “network of networks”
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
At “center”: small # of well-connected large networks
    “tier-1” commercial ISPs (e.g., Sprint, AT&T, Verizon), national & international coverage
    content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
    It's messier than a pure hierarchy - economics and politics shape it
Regional ISP
Regional ISP
Tier 1 ISP
Tier 1 ISP
IXP
Google
IXP
IXP

## Slide 19: Tier-1 ISP Network map: Sprint (2019)
links to/from Sprint customer networks
links to peering networks
to/from other Sprint POPs
…
…
…
…
…
POP: point-of-presence

## Slide 20: Roadmap
Review: What is the Internet? What is a protocol?
Network structure: how to build a “network of networks”
Layers and encapsulation/decapsulation
Notes: Bandwidth: capacity
Latency: delay
Loss: dropped packets
Jitter: variation in delay

## Slide 21: Internet layering: OSI vs. TCP/IP model
Transmission Control Protocol/Internet Protocol (TCP/IP) model:
  Practical model used on today’s Internet  Layers 5 (Session) + 6 (Presentation) are usually bundled into Application in TCP/IP
Different models, same idea  networking is layered abstraction, where each layer provides services to the one above
We follow the TCP/IP model (aka the Internet protocol suite model)to organize course content
3. Network
4. Transport
7. Application
2. Data Link
1. Physical
6. Presentation
5. Session
OSI
3. Internet (Network)
4. Transport
5. Application
2. Link
1. Physical
TCP/IP
IP, ICMP
TCP, UDP
HTTP, FTP, SMTP, DNS
SSL/TLS, JPEG, MPEG
RPC, NetBIOS
Ethernet, Wi-Fi
Typical Protocols & Technologies
Copper, Fiber, Radio
Notes: TCP/IP Layers Explain:
Physical Layer (Layer 1)
Pure hardware components: cables, fiber optics, wireless signals, connectors.
Transmits raw bits as voltages, light pulses, or radio waves.
Network Interface Cards (NICs) contain transceivers that handle this layer.
Data Link Layer (Layer 2)
Still close to hardware; often handled by NIC firmware and drivers.
Provides framing, MAC addressing, and error detection (e.g., Ethernet, Wi-Fi).
Mix of hardware and software: switches and NIC chipsets (hardware), drivers/protocol logic (software).
Network Layer (Layer 3)
Mostly software logic in the operating system.
Handles logical addressing (IP), routing, and forwarding.
Routers accelerate this with specialized hardware (ASICs).
Transport Layer (Layer 4)
Software-managed connections between applications.
Ensures reliable or best-effort delivery (TCP, UDP).
Runs inside the OS networking stack; some features can be offloaded to hardware (e.g., checksum).
Application Layer (Layer 5 in TCP/IP)
Directly visible to users and applications (HTTP, DNS, FTP, SMTP).
Includes higher-level logic like web browsers, servers, chat apps.
Can include encryption/compression (TLS, application data formats).

## Slide 22: Layer of the Network – Postal Analogy
CEO Alice wants to send a message to CEO Bob
Alice writes a letter
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
"Your days are numbered."

## Slide 23: Layer of the Network – Postal Analogy
Alice passes the letter down to her secretary
Her secretary puts the letter in an envelope
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
From: Alice, To: Bob
"Your days are numbered."

## Slide 24: Layer of the Network – Postal Analogy
Her secretary passes the letter down to the mailman
The mailman puts the envelope in a box
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
From: 123 Alice St
To: 456 Bob St
From: Alice, To: Bob
"Your days are numbered."

## Slide 25: Layer of the Network – Postal Analogy
The packet travels through the postal system, to Bob's building
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
From: 123 Alice St
To: 456 Bob St
From: Alice, To: Bob
"Your days are numbered."

## Slide 26: Layer of the Network – Postal Analogy
The mailman unwraps the box, revealing the envelope inside
The mailman passes the envelope up to the secretary
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
From: Alice, To: Bob
"Your days are numbered."

## Slide 27: Layer of the Network – Postal Analogy
The secretary unwraps the envelope, revealing the letter inside.
The secretary passes the letter up to Bob.
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
"Your days are numbered."

## Slide 28: Layer of the Network – Postal Analogy
As we move to lower layers, we wrap additional headers (and sometimes a trailer) around the packet  Encapsulation
As we move to higher layers, we peel off headers (decapsulation), revealing the inner headers
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
From: 123 Alice St
To: 456 Bob St
From: Alice, To: Bob
"Your days are numbered."
From: Alice, To: Bob
"Your days are numbered."
"Your days are numbered."
Notes: Internet packet encapsulation is the process where, as a data unit moves down the internet protocol stack, each layer adds its own protocol-specific header (and sometimes a trailer) to the data from the layer above it.
Decapsulation in networking is the process where a receiving device removes the header and trailer information added during encapsulation as the data packet moves up the network stack.

## Slide 29: Layer of the Network – Postal Analogy
Each person only cares about the headers at their layer
Mailman reads the green header, ignores all the payload inside
Each person communicates with its peers at the same layer
Alice's secretary writes the blue header, for Bob's secretary to read
A protocol at a specific layer only makes sense to people at that layer
Mail Room
Secretary
CEO
Mail Room
Secretary
CEO
Mailman only cares about this.
Secretary only cares about this.
CEO only cares about this.
From: 123 Alice St
To: 456 Bob St
From: Alice, To: Bob
"Your days are numbered."

## Slide 30: Layer of the Network – Postal Analogy
Notice: Different layers use different addressing schemes
Inside a building: “329 Diercks Hall."
In the postal system: “1025 N Milwaukee St, Milwaukee, WI 53202”
From: 123 Alice St
To: 456 Bob St
From: Alice, To: Bob
"Your days are numbered."
These addresses make sense to the mailman
These names make sense to the secretary

## Slide 31: Internet Headers and Encapsulation
Layer 2 Header
Physical
Link
Network
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 5:
Physical
Link
Network
Transport
Application
Layer 3 Header
Layer 4 Header
"Your days are numbered."
Converted to bits and transmitted
As we move to lower layers, we wrap additional headers around the packet

## Slide 32: Internet Headers and Decapsulation
Layer 2 Header
Physical
Link
Network
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 5:
Physical
Link
Network
Transport
Application
Layer 3 Header
Layer 4 Header
"Your days are numbered."
Bits received over wire
As we move to higher layers, we peel off headers, revealing the inner headers

## Slide 33: Layers and Protocols
Peers at the same layer communicate with each other using the header at that layer
HTTP, DNS
TCP, UDP
IP
Ethernet
Physical wire
Physical
Link
Network
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 5:
Physical
Link
Network
Transport
Application

## Slide 34: Application Layer: Next Lecture
Application layer builds services (e.g. websites, video streaming) on top of transport layer
This design lets us build different services, all on the same infrastructure.
Physical
Link
Network
Layer 1:
Layer 2:
Layer 3:
Move bits across space
Create links in a local network
Connect many local networks to form the Internet
Transport
Layer 4:
Reliably deliver packets, forming connections
Application
Layer 5:
Implement services on top of the Internet infrastructure.

## Slide 35: Summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  Routing versus packet forwarding
  Internet structure
layering, service , encapsulation
networks under attack
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!